## Slide 1: Scintilla Soldering Course
16 + (17) October 2023

## Slide 2: Planning
Lecture
What is soldering?
Electronic components
Soldering techniques
Finding and fixing errors
Principles of the kit
Practical
Planning your lay-out
Assembling your lay-out
Soldering the components
Testing
Debugging
Testing
Etc.

## Slide 3: What is soldering?
Breadboard
For testing
Temporary
Fragile
Not suitable for high frequencies
Soldering
Permanent
Rigid and proper electrical connections
Durable

## Slide 4: What is soldering?
Through-hole (THT)
Surface mount (SMD)

## Slide 5: Electronic Components
What to take into account?

## Slide 6: Resistors

## Slide 7: Capacitors

## Slide 8: Polarized Components
Long side usually ‘+’
White stripe usually ‘-’
Only possible to connect in 1 direction
+
-
+
-
+
-
*Not sponsored
** Not affiliated to Duracell do-group

## Slide 9: Help it has more pins!?

## Slide 10: Reading Datasheets
Maximum ratings
Common applications
Electrical characteristics
Pin layout(!)
What can you find?

## Slide 11: Transistor
B
C
E
Heat sink might be connected to one of the pins!

## Slide 12: Op-Amp

## Slide 13: IC Sockets
Easy to replace components
Prevents overheating during soldering
What are they used for?

## Slide 14: Soldering techniques
Do’s and don’ts

## Slide 15: Sorts of tin
Unleaded solder ~330°C
  Has an expiration date
  Uses flux core
Leaded solder ~230°C
  Higher melting point
  Toxic fumes
  Easier to solder
Flux
  ‘Repairs’ oxidized metals

## Slide 16: How to do it correctly

## Slide 17: Correct Joint

## Slide 18: Cold Joint
Solution: Reheat (and add new solder/flux)
Cause: cold metal

## Slide 19: Dry Joint
Solution: Reheat
Cause: Movement
during cooling

## Slide 20: Connections
Saves effort and solder
Use the components to make a bridge
Using Component Legs

## Slide 21: Connections
Connects nearby components
Use tin to make the connection
Using Solder Bridges

## Slide 22: Connections
Covers large distances
Makes circuit chaotic
Try to avoid these!
Using Wire Bridges
Very BAD example!!!

## Slide 23: Fitting Components
Make sure components are flush with the PCB
Avoid using wires
Do not connect the IC until after soldering
Keep it tidy!
Very BAD example!!!

## Slide 24: Soft Core Wires

## Slide 25: Finding Errors
And fixing them!

## Slide 26: Finding errors
Visual inspection
Voltage measurements at critical points
Follow the signal
Common errors:
  Missing connections
  Short circuits
  Cold joints
  Dry joints

## Slide 27: Visual Inspection
Fast and simple method to find faulty or missing connections
Clearly not finished

## Slide 28: Voltage measurement
Check DC first
Then follow the signal through the circuit
What voltages do you expect at every node?

## Slide 29: Fixing errors
Desoldering Pump
Desoldering Wick

## Slide 30: Audio Amplifier

## Slide 31: The Practical

## Slide 32: Jack Plug
Mono amplifiers only use the left channel
Ground
Right channel
Left channel

## Slide 33: Connecting the Jack

## Slide 34: Final Product
Analyse the circuit diagram
Make a layout on the PCB
Insert the components and solder them
How to get here?

## Slide 35: Final Product
Taking the schematic and placing the components on the PCB is very time consuming
This process will take (most of) the evening!
We have therefore also made a layout for you if you just want to solder!

## Slide 36: Documentation!
https://docs.scintilla.utwente.nl/masterclass/SolderingCourse2023
Or just https://bit.ly/soldercourse2023

## Slide 37: Good luck and happy soldering!
You can ask the MasterCLASS members for an example on how to solder a component.