## Slide 1: Scintilla SMD Soldering Course
March 10th

## Slide 2: Planning
Lecture
What is (SMD) soldering?
Electronic components
Soldering techniques
Principles of the kit
Practical
Soldering the components
Testing
Debugging
Testing
Etc.

## Slide 3: What is soldering?
Through-hole (THT)
Surface mount (SMD)

## Slide 4: Electronic Components
What to take into account?

## Slide 5: SMD components

## Slide 6: Capacitors

## Slide 7: Polarized Components
For through hole:
  Long side usually ‘+’
  White stripe usually ‘-’
For SMD Look on the PCB
  Usually says on the PCB
  Look for indents or marks on the components
Only possible to connect in 1 direction
+
-
+
-
-
+

## Slide 8: Help it has more pins!?
Orientation
  Almost always a indent
  Dot on the silkscreen

## Slide 9: Reading Datasheets
Maximum ratings
Common applications
Electrical characteristics
Pin layout(!)
Look for the indent on the package
What can you find?

## Slide 10: Soldering techniques
Do’s and don’ts

## Slide 11: Materials
Unleaded solder ~330°C
  Has an expiration date
  Uses flux core
Leaded solder ~230°C
  Higher melting point
  Toxic fumes
  Easier to solder
  Uses flux core
Flux
  ‘Repairs’ oxidized metals

## Slide 12: How to do it correctly
2025-04-01

## Slide 13: Correct Joint (THT)

## Slide 14: SMD soldering
First put solder on one pad
Place component
Heat first pad, then second pad and to finish again the first pad

## Slide 15: QFP chip
First attach corners
Dragging and cleaning up can be a way to do things

## Slide 16: SMD soldering
Extra flux can go a long way to help, it helps to prevent oxidation and help with flowing of the solder
Good example of using too much solder

## Slide 17: Start small
Use tweezers to place the components.
Start with large resistors and the small capacitors
Then work on the ic’s and led’s
Save the tall and through hole components until last!

## Slide 18: Go bigger
Use the techniques to solder the bigger components (mostly chips).
  Think smart about which one to place first.
Picture of bigger components on PCB

## Slide 19: Go through
Finish with the through hole components.
  Watch out for the polarity of caps and LEDs
Foto of through hole components

## Slide 20: Finding Errors
And fixing them!

## Slide 21: Finding errors
Visual inspection
  Common errors:
    Missing connections
    Short circuits
    Cold joints
    Dry joints
    Tombstoning

## Slide 22: Visual Inspection
Fast and simple method to find faulty or missing connections
Clearly not finished
Place picture of missing component

## Slide 23: Continuity measurement
Are all components connected?
Place picture of bad soldered connection

## Slide 24: Fixing errors
Flux
Desoldering Wick

## Slide 25: Principals of the circuit

## Slide 26: Principals of the circuit
USB
Timer
Counter
XORs
Demultiplexer
LEDs

## Slide 27: Principals of the circuit

## Slide 28: Good luck and happy soldering!
You can ask the MasterCLASS members for an example on how to solder a component. And all other questions 